## Slide 1: Part II
Introduction to Robot Code

## Slide 2: How to open a new FRC robot project
  Open LabVIEW.
  Click "FRC cRIO Robot Project" in the upper left section "New".

## Slide 3: Naming convention
  Name the project according to its function, not your name

## Slide 4: cRIO IP address
  Set the x's and y's in the IP address to match our team number: 0115.
replace this with:
10.01.15.02

## Slide 5: How to deploy code
  Open Project Explorer
  Hit the plus symbol next to Build Specifications
  Right click FRC Robot Boot-up Deployment
  "Deploy"

## Slide 6: Driver Station
Software and hardware

## Slide 7: Operations tab
  Shows the robot's battery voltage
  Shows the state of communication with the robot
  Shows whether code has been uploaded
  Shows whether stop button is connected
  Able to choose between teleoperated, autonomous and practice mode
  Enable and disable buttons
    The space bar will enable or disable the robot from any window
  Elapsed time since you enabled the robot
  Shows PC battery
  Can choose which team you are (red or blue)

## Slide 8: Diagnostics tab
  Shows the robot's battery voltage
  Shows the state of communication with the robot
  Shows whether code has been uploaded
  Shows whether stop button is connected
  Shows which joysticks are connected
  Shows whether an Ethernet link has been formed

## Slide 9: Stop button
  Acts as an emergency stop
    In general the program cannot be run without connecting the stop button
    Ctrl-Alt-Enter
  Connected by the USB hub to the computer
  Have to reboot the cRio after pressing the stop button
  Reboot Robot button no longer works after Stop button is pressed, so manual reboot is needed.
  Sometimes it does not work when plugged into the USB hub