## Slide 1: Part IV
Reading Power

## Slide 2: Power Distribution Board
  One green light for each power supply (+5V, +24V, +12V)
  Red light: a breaker is missing or blown

## Slide 3: cRIO
  Green power light
  Yellow status light
    Solid: no image
    Off: normal operation
  Ethernet port status lights (both ports)
    No lights: no connection
    Solid green: hardware connected and responding
    Yellow: software communicating
Ethernet ports

## Slide 4: Digital Sidecar
  One green light each for battery, +5V, and +6V
  Status light
    Fast blink: system error
    Off: cRIO has shut down or rebooted

## Slide 5: Solenoid Module
  Green status light

## Slide 6: Analog and Solenoid Breakouts
  Green power light

## Slide 7: Jaguar
  Solid yellow: neutral
  Blinking yellow: no communication, disabled
  Slow flashing red: fault
  Fast flashing green: forward
  Fast flashing red: reverse
  Solid green: full-speed forward
  Solid red: full-speed reverse
  No light: no power