## Slide 1: Wiring the new control system
MVRT
2010 – 2011 Season

## Slide 3: Basic Wiring Principles
Color convention for insulation (according to rules)
  Power = red, white, brown
  Ground = black, brown
Use right size (gauge/diameter) cables
  Big wire = smaller gauge = more current
Basic types
  Solid – single wire
  Stranded – multiple smaller wires twisted together
  Jacketed – multiple insulated wires with an outer cover

## Slide 4: FIRST Wiring Rules

## Slide 5: Robot Battery
12V Lead-Acid Battery
Connects to power block and main circuit breaker
Powers all functions of robot

## Slide 6: Wiring diagram
Battery

## Slide 7: Main Circuit Breaker
Turns robot on and off
To turn it off press the red button on the top
To turn it on close the switch
Connects the battery to the power distribution board
Normally use the red power cable from the battery to the breaker

## Slide 8: Wiring diagram
Battery
Circuit breaker

## Slide 9: Power Distributor Board
Distributes power to all the electrical components
Makes sure not too much current is drawn and everything is well connected
Connects to everything that requires power

## Slide 10: Wiring diagram
Battery
Circuit breaker
Power distribution board

## Slide 11: Compact RIO Controller (cRio)
Brains of Robot
Gets power from the power distributor board
Sends power and signal to the Digital Sidecard and the Wi-Fi interface
Connects via Wi-Fi to the driver station and the robot

## Slide 12: Modules and Bumpers
Analog Input Module
  Analog inputs with 3 pin connectors
Digital Adapter Module
  Connects to Digital Sidecar with a ribbon cable
  PWMs, Digital I/O, 3-pin relay connectors
Relay Module (On/Off)
  Control solenoids (electrical controller used with pneumatic system)

## Slide 13: Wiring diagram
Battery
Circuit breaker
Power distribution board
cRio controller
Digital module
Solen-
-oid module
Analog module

## Slide 14: Digital Sidecar
Used to connect variety of different signals, mainly to the Victors
Connects to the cRio module and power distributor block

## Slide 15: Wiring diagram
Battery
Circuit breaker
Power distribution board
cRio controller
Digital module
Solen-
-oid module
Analog module
Digital sidecar

## Slide 16: Jaguar Speed Controller
Determines how much power goes to the motor
Gets power from the distribution board, input from the digital sidecard, and outputs to the motors

## Slide 17: Motors
Motors wired to Jaguar speed controller
  Wired up by both the ground and the power
Wire with Powerpole connectors
Jaguars make motors move at a certain speed
Motors allow an object to rotate

## Slide 18: Spike
Input: a voltage input
Output: voltage to a motor
  Full forward (+12V)
  Full backward (-12V)
Turns compressor on and off to charge pneumatics system
Wired to compressor and digital sidecar

## Slide 19: Wiring diagram
Battery
Circuit breaker
Power distribution board
cRio controller
Digital module
Solen-
-oid module
Analog module
Digital sidecar
Motor speed controllers
Spike relays
Digital sensors
motors
compressor

## Slide 20: Linksys Wi-Fi Interface
Connects the cRio to the driver station/router
Connected to the OI and the power distribution board

## Slide 21: Wiring diagram
Battery
Circuit breaker
Power distribution board
cRio controller
Digital module
Solen-
-oid module
Analog module
Digital sidecar
Motor speed controllers
Spike relays
Digital sensors
motors
compressor
Pneumatic solenoid
Analog sensors
Wireless bridge

## Slide 22: WAGO & Sauro Connector
2 pole
Uses – Power distributor to…
  bumpers
  gaming adapter
  Digital side card
Sauro Connector
4 pole
Uses – Power distributor to…
  cRio

## Slide 23: Other parts/tools used to wire the robot
Servos
Electrical tape
PWM Wires
Zipties
Label Makers

## Slide 24: Servos
Rotates from 0 to 254
Once given position, stays there and cannot be moved unless “told” by the code
A very small motor

## Slide 25: Servo 2011
2011 changes - Can use more servos starting this year
Max power = (0.5 * stall torque) * (0.5 * no load speed)
  Load speed has to be less than 4W
Example (Hitec Hs – 322 servo)
  Servo max power rating = torque x speed x unit conversion factor
  Torque = 3/7 kg/cm = 0.36 NM
  RPM = 0.15s @ 60 = 66.7 RPM
  0.36 NM x 66.7 RPM x 0.1047 = 2.5W
Speed (4.8V/6.0v) | 0.19/0.15 sec @ 60
Torque oz/in (4.8V/6.0V) | 42/51
Torque kg/cm (4.8V/6.0V) | 3.0/3.7

## Slide 26: Electrical Tape
Prevents the electrical current from hurting people on battery terminals or open wire
Primarily used to insulate bare wires or ends
  use red electrical tape for power wires
  Use black tape for ground wires
Use to cover jaguar terminals

## Slide 27: PWM
Stands for pulse width modulator
Used to transmit data to speed controllers
Red - power
Black - ground
White/Yellow - signal

## Slide 28: Zip ties
Used to keep wiring neat and out of the way from moving parts to avoid the wires from getting cut

## Slide 29: Label Maker
Labeling wire makes it easy to identify where it’s from / going to
  Ex. label pwm cables from digital sidecar to jaguars